## Slide 1: Seminar 5
06th May 2016, Tran Viet Cuong

## Slide 2: 2 weeks
Finding MCU
Finding ECG sensor (Dry contact)
EMG signal

## Slide 3: MCU
For wearable device, MCU needs:
  Low-Power
  Fast enough to operate standalone system
How to know MCU whether is enough to operate:
  ROM
  RAM
  CPU

## Slide 4: MCU
MSP432P401R LaunchPad:
  Ultra Low Power
  48MHz
  32-bit ARM Cortex M4F with Floating Point Unit and DSP acceleration
  256KB Flash
  64KB RAM
  24ch 12-bit ADC
  Comparator
  4 16-bit, and 2 32-bit Timers
  Up to 4 I2C, 8 SPI, 4 UART

## Slide 5: ECG sensor (Dry contact)
PS25205B (EPIC sensor)
  Low current 1.4mA
  Dry-contact capacitive coupling
  Operates with bipolar power supply from ±2.4V to ±5.5V

## Slide 6: ECG sensor

## Slide 7: ECG sensor

## Slide 8: ECG sensor

## Slide 9: EMG signal
EMG signal property:
  Non-stationary
  Nonlinear
  Complexity
  Large variation
To make a system based on EMG first we need to extract the features of the acquired EMG signal based on which it can be further classified for purpose (ex. Various hand movements).
Common features for classifying EMG signal: mean absolute value, varience, standard deviation, maximum value, zero crossings, …

## Slide 10: EMG signal
EMG signal processing:
  Wavelet analysis
  Autoregressive model
  Artificial intelligence
  Higher-order statistics
  others

## Slide 11: EMG signal
Artificial intelligence (based on Neural Networks)
  Useful for real-time application (EMG signal recording and analysis)
  EMG signal features are first extracted through Fourier analysis and clustered using fuzzy c-means algorithm (method of clustering which allows data to belong to 2 or more clusters)
  Fuzzy logic systems are advantageous in biomedical signal processing and classification

## Slide 12: Next 2 weeks
Fuzzy logic system
Try to extract EMG signal features

## Slide 13: Thank you!!!

## Slide 14: Question??

## Slide 15: MCU
Run a floating point multiplication 1,000,000,000 times. CPU performance, 14 Mflops (7MHz)
Not need memory access all the time, this should need less memory access then the performance less than 25MFops